ARCHITECTURAL WORK
IN FREECAD 0.21.2

Introduction
What is FreeCAD
Free CAD is a parametric 3D Modelling program with 2d Drafting capabilities. For this tutorial you will learn how to / create 2D drafting objects and how to arrange them on a virtual paper for plotting / create 3D models and Extract 2 projections and that can be used in plotting

This is the starting page that appears when first starting FreeCAD . The table below explains each annotated item. (this remains the same until the settings are changed it contains sample files that show the capabilities of the software.
Menu items	Description	Tips
Combo view (1)	The combo view consists of 2 tabs; Model and tasks. / The Model tab shows the list of current objects with subsections on data and view / data: displays the physical properties of an object such as length / the view tab displays the objects appearance such as line thickness and colour / the task tab displays the current action the user is making it varies depending on the task being done.

Navigation style (2)	Displays the current ways to; pan, zoom, select and Rotate the view	Hovering the cursor of the current navigational style, displays the current mouse and keyboard commands.
Tool Bar (3)	Displays the current tools of the active work bench
Current Work Bench (4)	This displays the current work bench. Work benches are a set of tools used to perform certain tasks	The primary workbenches being used are the; Draft, Arch and Tech Draw work benches.
Drop Down Menu (5)	Standard options	It is always displayed

Work Benches
What is a work bench / A work bench is a collection of tools used to perform certain tasks. In this tutorial the work benches that will be focused on will be the draft work bench, the arch workbench and the tech draw workbench.
Draft work bench		This is a collection of 2d drafting tools , including; points, lines , poly lines, circles , other geometric shapes and the means to dimension and modify them.
Arch work bench		Has some cross over with the draft work bench, it is a collection of tools that deals primarily with the creation of building components such as wall, slabs roofs and windows.
Tech draw work bench		This is a collection of tools used to place 2d drawings and views of 3d objects on to a virtual representation of a paper . Here drawings from different workbenches can be scaled, rotated and further annotated.

Conventions And Shortcuts
Mouse
Left handed layout / middle/ orbit / options	Right handed layout
options / middle/ orbit / select	select

Keyboard
Function	Command	Icon	Tips
Multi select	Ctrl,+ select	-
Box select	Shift+e	-	Click once and move mouse over objects
Zoom in and out	Ctrl + middle + (move mouse)	-	These commands vary per the navigation style hovering your mouse of the current style will reveal how to navigate.
Pan view	Shift + middle (mouse move)	-
Create Point	Has no keyboard shortcut. Select it in the tool bar		Geometry can be created in multiple ways / Selecting points arbitrarily/ with appoints / Entering coordinates in the task view of the combo menu
Create line	Select the icon or,press ‘l’ then ‘i’
Create Poly Line	Select the icon or,press ‘p’ then ‘v’

Create circle	Select the icon or, Press ‘m’ then ’v’ , select pivot, select destination The first point determines it’s location and the second determines / its radius from that point.		These methods can be mixed and matched depending what needs to be done. / Created objects can also be modified in the combo view. The specifics of which will be shown later in the tutorial
Create ellipses	Select the icon or, / press ‘e’ then ‘l’ the first point determines it’s start and the second how long it is.
Create Arcs	Select the arc icon in the tool bar, there are two ways to create an arc: / selecting three points / selecting a centre and radius then two points.
Create Rectangle	Select the icon or, press ’r’ then ‘e’.
Create Polygon	Select the icon or press ‘p’ the ‘g’
Create Beziér	Select the icon, you can create n curves and/ cubic curves / you may select each point manually
Create B- Spline	Creates a multi point B spline. You can select each point where it bends.

Move Object	Move an object by selecting a reference point then select a destination point (select using your mouse)
Rotate Object	Rotate an object using a reference point
Offset Object	this offsets objects depending on the position of the cursor, press ‘o’ then ‘s’ or select the icon in the tool bar
Mirror Object	This Mirrors an object along a line. Press ‘m’ then ‘I’
Trim Object	Press ‘t’ then ‘r’ / This shortens or increase the length of a line (can be a poly-line segment)		You may select an object before or after the command
Hiding/Revealing An Object	Press the space Bar	-
Box Select	shift+B
Box Element Select	Shift+ E

Snap Points
Snap points exist on all geometries one creates. To activate snap points key in shift+s the snap icon will appear as shown:
this indicates that snap points lock is on. Pressing shift+s turns these snap points off.
End points		The snaps to the end points and vertices of 3d and 2d objects
Mid point		This snaps to the mid point of a line
Centre		This snaps to the centre of a shape
Intersections		This snaps to intersecting, meeting or overlapping geometries
parallel		When creating lines creates a snapping point parallel to an existing line or object
snap working plane		Projects snap points onto current working plane
Grid snapping		This snaps the cursor to points on the grid
Ortho snapping		This snaps the cursor to vertical, horizontal or 45 degrees when drawing geometry

Preferences and defaults
The Preferences menu displays the settings and defaults for work benches and other more General settings
1 / 2 / 3 / 4 / 5 / 6 / 7 / 8
Items	Function	Tips
General (1)	For adjusting the default units and language preferences	-
Display(2)	Changes the rendering and colour settings.	For 2d drafting use a simple light grey colour for the background for good visibility.
Python(3)	Can be used to create Macros and custom commands	Macros can automate repetitive processes
Add-on Manager (4)	Can be used to add more workbenches and	Note that some work benches are still being tested
Import- Export (5)	Mainly going to be used to convert files to dxf, pdf as well as importing these file types	The c++ exporter/importer is faster but has list features that the python exporter/importer
App Image (6)	It is used to get updates for the FreeCAD	-
Work Bench options(7)	Contains a set of options unique to each work bench, such as defaults for objects.	Make sure the workbench you want to edit is active

Setting Up FreeCAD Defaults
Steps	Navigation
Ensure the Draft workbench is active / In the drop down menu	select edit>Preferences

Under General select the appropriate units for this tutorial we will use the standard setting so we can draw in mm	(general>general-tab>unit system> standard(kg,mm,s, degree))

Change the Background colour from the default linear gradient to a simple colour	Edit> preferences> Display>colours> background colour> simple background colour / select the colour square and adjust it to a light grey colour

Opening and Navigating a File
Tutorial I Part I
Steps	Navigation
On the drop down menu select file then open (ensure the draft workbench is selected) *	select file>open>new> / workbench>Draft
Select the pre-existing project Draft tutorial	Windows c/programfiles/FreeCAD/Arch TutorialI.FCStd / Linux:home/.local/share/FreeCAD/ArchTutorial
2 / 1 / 3 / 5 / 4
Components	Description
Page(1)	Virtual paper
Folders(2)	Container for a set of objects
File Tabs(3)	The active open files
Current view (4)	The current plane you are viewing
Current view(5)	The current plane you are drawing on
Pan through the drawing	(see shortcuts by hovering cursor over navigation style

Tutorial I Part II
steps	Navigation
Set the Work Bench to Draft	Select the current work Bench icon and change it to the draft work bench
Set the current view to the Top view	The current plane is shown in the top right corner and can be accessed by the following shortcuts; / press 5 for the Bottom view / press 4 for the Rear view / press 3 for the Right view / press 2 for the Top view / press 1 for the Front view
Set the working plane to the top working plane	Select the working plane icon and choose the top plane
Zoom in on the Floor plan	Varies per Navigation style, hover your mouse over the navigational style to display the shortcuts/commands
Pan in on the floor plan

Select the folder in the combo view titled floor plan	Select using your mouse’s cursor
Hide the floor-plan / Reveal the Floor plan	Select the Floor plan folder in the combo view with your cursor and then press the space bar when it is highlighted / Items can be revealed by pressing space-bar once more, select the hidden item in the combo view and press the space bar on the keyboard once more.

The Floor plan will disappear
You can also delete items in the combo view / delete the floor plan	Select the floor plan in the combo view and press the delete button on the keyboard
Undo the deletion	Most actions and tasks can be undone by pressing Ctrl z
Expand the groups in the combo view	select the arrow icon next to the floor plan group

This will display all the components within the folder
Similarly you can Hide and reveal components / Hide wire 36794	Press the space bar after selecting an object in the combo view.
Delete wire 36794	Select the wire in the combo view and press delete
Undo the deletion	Press Ctrl z
If you have trouble finding the object in the combo view you can search for it	Option click on the top of the combo view > (select) selection view, / you can enter the name of an object in the selection view / option / option select the results of the search and go to selection / this highlights the object in the combo view
Select a portion of the floor-plan	Selecting multiple objects can b done with the box select tool / shift E selects all objects / Shift B selects all objects of a specific type

Press shift+e and select the starting point: drag from the starting position to cover some of the floor-plan / (note that after pressing shift+r you cannot pan or zoom while box selecting / so be sure to zoom to the appropriate view)

The selected items will be highlighted In the view
They will also be highlighted in the combo view
You can / Delete the selected objects / Hide the selected objects / And modify their properties in the combo view
This ends the navigation portion of the tutorial

#
Creating Geometry
Tutorial 2
Creating documents and preparing a file / 1 / 3

Select file>new / This creates a new document / select the work bench button and select the draft work bench
Snap points and views setup / Set the view to the top by pressing ‘1’ / turn the active working plane to top / This ensures objects are only drawn in one plain. / Select the snap point / Select snap working planes	5 / 4 / 6

creating points / points are made by first by: / selecting the icon in the tool bar menu / the combo view will appear, they can be placed by either / selecting anywhere in the drawing plane (press the select button on the mouse anywhere) / entering coordinates in the combo task view / using snap points to place it on another object ( in this case use the grid snap)

CREATING POINTS
TASK	STEPS
Create a point (A) at the origin, there are three options Arbitrary, and using the combo view with or without snap points	Select the point icon
Create the point and move it later	select the created point / in the combo menu>Model / select the data tab.

Input coordinates	Under draft in x, y and z / enter 0 mm
Or Snap point	Select the grid snap icon>hover it over the origin and the icon will appear / select the position with the cursor

Combo view
Creating a point at the origin	Select point icon>Combo menu>tasks / inter 0 for each coordinate

CREATING LINES
TASK	STEPS
Create a line from the origin at length 1000 mm 45 degrees	Combo Menu / l,i / for x y and z enter / press enter / select the angle option / this locks in the angle / enter 45 / for length enter 1000 mm / press enter / Arbitrary Line / l,i / select first point / select second point / select the line / combo view>models>data>start / for x, y and ,z enter 0 mm / view>models>data>end / for x and y enter 1000 for z enter 0 / view>models>data>length / enter 1000 mm / l,i / turn these snap points on :

Create a line from the origin at length 1000 mm 45 degrees	Hover over the created point ‘A’ / the snap point point appears / select with your mouse / move the cursor until the Ortho icon appears / move the cursor to the nearest / point on the grid at 45 degrees. Ortho snaps to vertical horizontal or 45 degrees / select with the mouse when the grid snap point icon appears / in actual practice these methods are mixed and matched where appropriate

CREATING POLY LINES
TASK	STEPS
Create a poly line with three segments / each segment should be 2000 mm long and at 90 degrees to each other. The starting point should be the point ‘A’	Combo View / each segment needs a start and end point / ‘p’,’l’ / combo view>tasks / for delta x y and z enter 0 / press enter / for delta x enter 0 mm / for delta y enter 2000 mm / for delta z enter 0 mm / press enter/ select enter point / 0for delta x enter 2000 mm / for delta y enter 2000 mm / for delta z enter 0 mm / press enter/ select enter point / for delta x enter 0 mm / for delta y enter -2000 mm / for delta z enter 0 mm / press enter/ select enter point / press esc/ select close with the cursor

ARBITRARY / press ‘p’ then ‘l’ or select the poly-line icon / select any where on screen 4 times / select the wire press the down grade button/ type d then n do this twice while the object is selected / this creates 3 edges / press u then p / select the upgrade icon while each is selected / this creates three lines / select one of the lines / > combo view>model> data> property >start / for x,y and z enter 0.0mm / > combo view>model> data> property >end / for x enter 2000 mm / for y enter 0 mm / for z enter 0 mm / select another line / > combo view>model> data> property >start / for x enter 0.0 mm / for y enter 2000.0 mm / for z enter 0.0 mm / > combo view>model> data> property >end / for x enter 2000.0 mm / for y enter 2000.0 mm / for z enter 0.0 mm / Select the last unmodified line / > combo view>model> data> property >start / for x enter 2000.0 mm / for y enter 2000.0 mm / for z enter 0.0 mm / > combo view>model> data> property >end / for x enter 2000 mm / for y enter 2000 mm / for z enter 0 mm / > combo view>model> data> property >length / enter 2000 mm / Shift+e select the 3 lines / press u then n or select upgrade

Snap points / turn on the following snap points / Select Grid snap / enter p then l / as each box in the grid as pre configured is 1000 mm by 1000 mm / one can / select at the origin / select two grid units up from the origin / select two grid units to the right from the previous point / select two grid units down from the last point selected.

CREATING CIRCLES
TASK	STEPS
	Combo view / enter ‘c’ then ‘I’ or select the circle tool in the tool bar / combo view>tasks / for delta x enter 0 / for delta y enter 0 / for delta z enter 0 / press Enter/ select enter point / for the radius / enter 2000 / press enter

ARBITRARY / enter c then I / select the make circle icon in the tool bar / select with the mouse / the first point / (the circles centre / Select with the mouse again / (the radius) / Combo view>Model>Data / under draft select the radius and enter 2000.0 mm / under Base go to placement / for position x enter 0.0 mm / for position y enter 0.0mm / for position z enter 0.0 mm / Snap Points / tun on point snap / turn on Grid snap / type in ‘c’ then ‘I’ / hover the mouse over the point previously created / the point snap icon will appear / select with your mouse / whilst it is visible / move your cursor to the right / so that the radius shown in the combo view is 2000.0 mm / selecting the bottom right corner of the square creates a circle of radius 2000.0 mm / select the created arc / .combo view>model>

CREATING ARCS
TASK	STEPS
Make and Arc with a radius / 1000 and an aperture angle of 90 / and a start angle of 180 / It should be placed at coordinates / (-2000mm, 0.0 mm, 0.0mm) / The arc tool is useful when showing the swing of a door in a floor-plan	Combo view / Select the Arc button / combo view > tasks / in the local delta x enter 2000.0 / in the local delta y enter 0.0 / in the local delta 0.0 mm / select enter point with mouse/ Enter / for radius 1000 mm / 180 for the star angle / press enter / 90 for the aperture angle / press enter / Arbitrary / select the arc icon / select on the screen 4 points / the first decides the arcs centre / the second the radius of the arc / the thirds its starting angle / the fourth its aperture or ending angle / Select the arc / Combo view>Data> / under Draft / select Radius and type in 1000 / select first angle and type in 90 / select the second angle and enter in 180 / under Placement / Angle should = 90 / position should be / x=2000 mm / y= 0.0 mm / z=0.0 mm

snap points / turn on Grid snap / select the arc symbol in the tool bar / select the bottom most intersection of the circle and square (2000,0,0) / Select 1 square away (radius of 1000 mm) / hover your cursor over a grid square away from the the radius ( the start angle in the combo view should read 90 / select that point with your mouse when the grid snap symbol appears / select a point inside the circle 1 grid square away from the radius of the arc / ( be sure to move your cursor anti clockwise)

CREATING ELLIPSES
TASK	STEPS
Create an ellipses that intersects with the circle arc and goes through the origin	COMBO VIEW / Press ‘e’ then ‘l’ / combo view> tasks / for local delta x enter -2000.0 / for local delta y enter 1000.0 mm / for local delta z enter 0.00 mm / select enter point/ press ‘Enter’ / for local delta x enter 4000.0 mm / for local delta y key in 1000.0 mm / for local delta z key in 0.0 mm / press enter/ select enter point / ARBITRARY / press ‘e’ then ‘l’ / select a starting point / Select a ending point / select the ellipses / combo view> model>data / Draft>for minor radius enter 500.0 mm / Placement>position / for x enter 0.0 / for y enter -500.0 mm / for z enter 0.0 mm / snap points / make sure grid snap points are on / pre ‘e’ then ‘l’’ / hover the cursor over a point outside the created circle / from the origin select a point on the grid 2 grid units to the right / select it with the cursor / from the origin select a point 2 units to the left and 1 unit down from the origin .

CREATING POLYGONS
TASK	STEPS
Create a regular polygon with 6 sides that sits inside the circle. This tool is useful for creating the basis for the external walls of a building quickly	COMBO VIEW / press ‘p’ then ‘g’ / Combo view> Tasks / for local delta x key in 0.0 mm / for local delta y key in 0.0 mm / for local delta z key in 0.0 mm / Select enter point/ press ‘Enter’ / for sides enter 6 / for radius enter 2000.0 mm / this tool is mostly used with the combo view / you can however use snap points to select a centre point

CREATING B-SPLINES
TASK	STEPS
Create a B spline that connects a vertices the point at the origin and another vertices / B splines are useful for creating more organic designs.	Press ‘b’ then ‘s’ / Combo view>task Select the ellipses / for delta x enter -2000.0 mm / for delta y enter 0.0 mm / for delta z enter 0.0 mm

THE TRIM TOOL
TASK	STEPS
Extend the 45 degree line to / the edge of the circle	COMBO VIEW / Select the line on the side you wish to extend( the side closer to the circumference of the circle / press ‘t’ then ‘r’ / enter 1000.0 mm / press ‘Enter’ / ARBITRARY / select the line / enter ‘t’ then ‘r’ / move the mouse outside of the circle top right) / select with your mouse / select the line / combo view> model>data / Select length / make it 2000.0 mm / SNAP POINTS / select snap point point on / select the snap intersection point / select the diagonal line / enter ‘t’ and ‘r’ / move the cursor past the square and select / while holding the ‘Ctrl” key / select the line again / enter ‘t’ then ‘r’ / Move the cursor while holding control / select with your mouse when the line intersects with the circle

THE MOVE TOOL
TASK	STEPS
Move the six sided poly gone 1000 mm in the x axis around the six sided	COMBO VIEW / Select the six sided polygon with the cursor / enter ‘m’ then ‘v’ / select the reference point / in this case / for local delta x enter -2000 mm / for local delta y enter 0.0 mm / for delta z enter 0.0 mm / press ‘x’ / for delta x enter 1000 mm / press ‘Enter’ / ARBITRARY / select the six sided polygon / enter ’m’ then ‘v’ / press ‘x’ / select a reference point anywhere / select anywhere to the right / of the polygon / press ‘Ctrl’ then ‘z’ / SNAP POINTS / turn snap point grid on / turn snap point point on / Select the six sided polygon / enter ‘m’ then ‘v’ / hover your mouse over the Right most Vertex of the polygon / when the snap point icon appears select with your mouse / enter ‘x’ / move the cursor 1 grid unit from the previously selected point / when the gird snap icon appears select with your mouse.

THE MOVE TOOL
TASK	STEPS
Rotate the ellipses 90 degrees about the origin	COMBO VIEW / Select the ellipses / and enter ‘r’ then ‘o’ / combo view> tasks / for delta x enter 0.0 mm / for delta y enter 0.0 mm / for delta z enter 0.0 mm / press enter after enter each / for the base angle enter 0 degrees / press enter / for the rotation angle enter 90 / ARBITRARY / Select the ellipses / and enter ‘r’ then ‘o’ / select any where to select the pivot point / hold shift and select with the cursor / move the mouse to adjust the rotations / hold shift after moving the mouse / to get rotation angle in increments of 90 degrees / press ‘Ctrl’ + ‘z’ / SNAP POINTS / select the point snap and grid snap in the toolbar / select the ellipses / press ‘r’ then ‘o’ / select the point at the origin / move the cursor until the base angle line is horizontal / hold shift and select with the mouse / move the mouse upwards / hold shift / the ellipses while move around showing a preview of what it would look like. / Select with your mouse.

THE SCALE TOOL
TASK	STEPS
Scale the six sided polygon to 3 times their original size. This is use for quickly changing the scale of objects imported that were scaled incorrectly.	COMBO VIEW / Select the hexagon / press ‘s’ then ‘c’ / Combo View> Tasks / select uniform scaling / select working plane orientation / select create clone (the clone function will be explained later in the tutorial) / for scale factor x enter 3 / note that this sets the y and z scale factors to 3 as well / this is because uniform scaling was selected / ARBITRARY / select the hexagon / press ‘s’ then ‘c’ / select any where on the screen / combo view >tasks> scale / select pick from/to points / select 1 grid unit from the previously selected point and then two units from that point. / Press ‘Ctrl’ + ‘z / SNAP POINTS / turn point snap on / turn grid snap on / select the hexagon / press ‘s’ then ‘c’ / select one of the vertices on the hexagon / select / select from points / select 1 grid unit from the vertices you selected / select two units from the select you just made / this makes the scale factor 3

THE MIRROR TOOL
TASK	STEPS
Create a mirror image of enlarged hexagon, using a vertical line through the origin.	COMBO VIEW / Select the enlarged cloned hexagon / press ‘m’ then ‘I’ / Combo view>task> Mirror / for local delta x enter 0.0 m / for local delta y enter -10.0 m / for local delta z enter 0.0 m / press ‘Enter’ three times to accept each position / this selects the first point of the mirror/’select’ select point with your cursor / Combo view> Tasks> Mirror / for local delta x enter 0.0 m / for local delta y enter 20.0 m / for local delta z enter 0.0 m / Press ‘Enter’ three times to accept each position/ ‘select’ select point point with your cursor / ARBITRARY / Select the enlarged cloned hexagon / press ‘m’ then ‘I’ / select two points anywhere / these two points for the invisible line of the mirror / SNAP POINTS / turn on point snap and grid snap in the tool bar / Select the hexagon / and press ‘m’ then ‘I’ / select a point on the grid in line with the origin / select a point on the grid in line with the origin

THE OFFSET TOOL
TASK	STEPS
Offset the circle inwards by 1000.0 mm. Useful for adding thickness to b-splines	COMBO VIEW / Select the circle created at earlier stages of the tutorial / press ‘o’ then ‘s’ / move the cursor inside the circle / Combo View> Tasks> Offset / select the copy option / press enter. / ARBITRARY / Select the A line / press ‘o’ then ‘s’ / move the mouse to indicate which direction you would like to offset the line / ‘select’ with your mouse to place the offset of the line / press ‘Ctrl’ +’z’ / SNAP POINTS. / select the line / assure point snap is on / assure grid snapping is on / press ‘o’ then ‘s’ / move the line about 1 grid unit away from the original line / when the grid snap symbol appears next to the cursor select with the mouse.

DIMENSION TOOL
TASK	STEPS
Dimension the exterior of the outer two polygons as shown in the image below	Select an edge and press ‘d’ then ‘I’ / moving / for delta x enter 0 mm / for delta y enter 2000 mm / for delta z enter 0 mm / do this for all the exterior edges / Combo view> Model / press ‘ctrl’ + select / and click on each dimension in the combo view / press the spacebar to hide them

ARCH WORKBENCH
THE WALL TOOL
TASK	STEPS
Create a wall at the origin of length 3000 , width 220 and height 3000 / (it should be parallel with the y axis) / use the open rectangles geometry to create a wall	COMBO VIEW / Press ‘w’ then ‘a’ / combo view> tasks / for local delta x enter 0.0 mm / for local delta y enter 0.0mm / for local delta z enter 0.0mm / select enter point / / press y / enter 3000 / under wall options / length should read 3000 mm / width = 220 / height = 3000 mm / alignment= centre / select enter point / press ‘Ctrl’ + ‘z’ / ARBITRARY / press ‘w’ then ‘a’ / select any where on the drawing / select any where on the drawing / select the created wall / Combo View > model >Data / press ‘Ctrl’ then ‘z’ / SNAP POINTS / press ‘w’ then ‘a’ / assure Grid snap is selected / assure Snap point is selected / combo view> Tasks> wall options / select the point at the grid origin / assure / width= 220 mm / height = 3000 mm / Alignment = centre / select the point 3 grid units above the origin.

	USING EXISTING GEOMETRY / Select the open rectangle / press ‘w’ then ‘a’ / this uses an existing shape as a base / note that in / Combo View> Model> Data / this element is still viewable and modifiable
1 / 3 / 2
	1: sub element of the wall / 2: walls to be joined / 3 : Arch Add button

THE ARCH ADD TOOL
TASK	STEPS
Fuse the walls create walls into 1 model	While holding ‘Ctrl’ Select the two walls press the add select button in the tool bar .

THE STRUCTURE TOOL
TASK	STEPS
Create a slab inside the innards of the walls	-1780.0 / 1890 / select the structure tools / Combo view>Tasks> structure options / select / category = blank/none / for height 110 / for 945 / -3000 / Press ‘r’ then ‘e’ / Combo view> Tasks / for delta x enter 1890 mm / for delta y 1890 mm / for delta z 0 mm / select enter point / for the second point / for delta x enter 1780 mm / for delta y enter -1890 mm / for delta z enter 0 mm / Select enter point / this creates a rectangle at height 100 mm / select the rectangle / select the Arch Structure tools

THE STRUCTURE TOOL
TASK	STEPS

Create Gable roof that covers the walls	Press ‘r’ then ‘e’ / 1890 mm / 0 mm / 3000 mm / select enter point / 2220 mm / 3000 mm / 0 mm / select enter point / select the rectangle / press ‘r’ then ‘f’ / Combo view> model> / double select the roof object / this opens its property table / set all angles to 15 mm / set all runs to 1200 mm / Combo view> Tasks / select close

THE WINDOW TOOL
TASK	STEPS
Create a window on the right face of the model.(1000 by 1500 mm)	COMBO VIEW / Combo view> Tasks / Make the side the Select the right face / for delta x input 575 mm / for delta y input 1500 mm / for delta z input 2110 mm / select the fixed preset / select enter point / This adds the wall as a host object to the window / ARBITRARY / set the current working plane to side / select the Right face / press ‘w’ then ‘n’ / select any where on the face of the wall / (the window tool uses the last dimensions and presets when using this tool) / press ‘ctrl’ z / SNAP POINTS / et the current working plane to side / select the Right face, the select the current working view button / turn grid snapping on / press ‘w’ then ‘n’
Create A custom window on the left hand side of the building

DRAWING A FLOOR PLAN
TASK	STEPS
Open the base base of the floorpan	File> Open> c/programfiles/FreeCad/Tutorials / File>Open >local/share/FreeCad/ Tutorials
Create the building footprint	Press ‘p’ then ‘y’ and select the following points in order ; A,B,C,D,E,F,G,H,J,K,L,M,N,O,P,A to form a closed polygon (PY1) / select the line / combo view>Model>Data / Make face= false / Select the poly line again and press f2 or option click the item and select rename it / Key in PY1 / note the poly line will be in a group titled construction

Create the roof line and slab outlines	Press ‘p’ then ‘y’ and select the following points in order; A, B, C, D, E, F, G, H, I, K,L, A / select PY 1 in the combo view under construction / press o then s, move the cursor inside the shape and key in 220 mm in combo view > Tasks / Combo view tasks option select the newly created poly line and select rename / rename the line to py3

Create the roof line	select py 2 and key in o,s, move the cursor out side of the poly line and key in 300 mm / press enter / combo view model / option select line select rename / rename line to py3, press enter / combo view> Model / option click on the poly line and select rename enter py3 and press enter

select py 3 and key in o,s. Move the cursor outside of the shape, Key in 300 mm in the task tab on the right of the screen press enter / combo view> Model / select the poly line / select the new line and rename it as py4 / select the poly line py4 and press ‘o’ then ‘s’ enter 300 mm and press enter, ( move sure to hover the mouse out side of the boundaries of the selected line. / combo view > Model / select the newly created poly line in the combo view / option select the poly line and select rename / type in PY 5

Add the existing wall block	press shift r while the view space is at ‘wc/shower’ / press shift+ E and select the object / key in m,v and click on the left most corner

Sketching in the inner walls	key in r,e and create rectangles of the following dimensions (each representing the size of a room. / Navigate and pan to the points using your preferred navigation style / press ‘r’ then ‘e’ / with point snap on

Select the corner as shown / for delta x input 3000 mm / for delta y input 2300 mm / for delta z input o mm / press enter confirming each option/ select enter point
press ‘r’ then ‘e’ / select the corner shown / for delta enter 1880 mm / for delta y enter 1690 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point
press ‘r’ then ‘e’ / select the corner shown / for delta enter 1010 mm / for delta y enter 1690 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / select the corner previously selected / press x (to restrict to x axis / for delta x enter 110 mm / selected enter point/ press ‘Enter

M
press ‘r’ then ‘e’ / select the corner shown / for delta enter 3000 mm / for delta y enter 3500 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / select the corner previously selected / press x (to restrict to x axis / for delta x enter 220 mm / selected enter point/ press ‘Enter
press ‘r’ then ‘e’ / select the corner shown / for delta x enter 2400 mm / for delta y enter 600mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / select the corner previously selected / press x (to restrict to x axis / for delta x enter 220 mm / selected enter point/ press ‘Enter
press ‘r’ then ‘e’ / select the corner shown / for delta x enter 490 mm / for delta y enter -600mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / select the corner previously selected / for delta x enter 220 mm / for delta y enter -110 mm / selected enter point/ press ‘Enter

press ‘r’ then ‘e’ / select the corner shown / for delta x enter 1800 mm / for delta y enter 2400 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / select the corner previously selected / press x (to restrict to x axis / for delta x enter 110 mm / selected enter point/ press ‘Enter
press ‘r’ then ‘e’ / select the corner shown / for delta x enter 1800 mm / for delta y enter 990 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / select the corner previously selected / press y (to restrict to y axis / for delta y enter 110 mm / selected enter point/ press ‘Enter

press ‘r’ then ‘e’ / select the corner shown / for delta x enter 600 mm / for delta y enter 1800 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point
press ‘r’ then ‘e’ / select the corner shown / for delta x enter 600mm / for delta y enter 600 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / select the corner previously selected / press x (to restrict to x axis / for delta x enter 110 mm / selected enter point/ press ‘Enter
press ‘r’ then ‘e’ / select the corner shown / for delta x enter 600mm / for delta y enter -390 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / select the corner previously selected / press y (to restrict to x axis / for delta x enter 110 mm / selected enter point/ press ‘Enter

press ‘r’ then ‘e’ / select the corner shown / for delta x enter 2290mm / for delta y enter -4000 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / selected enter point/ press ‘Enter
press ‘r’ then ‘e’ / select the corner shown / for delta x enter 4000 mm / for delta y enter -3100 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point
press ‘r’ then ‘e’ / select the corner shown / for delta x enter -5560 mm / for delta y enter -3000 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point

Navigate to the right side of the building by panning / press ‘r’ then ‘e’ / select the corner shown / for delta x enter 5030 mm / for delta y enter -4640 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point
press ‘r’ then ‘e’ / select the corner shown / for delta x enter -3610 mm / for delta y enter -3000mm / for delta z enter 0 mm / press enter confirming each option/ select enter point
press ‘r’ then ‘e’ / select the corner shown / for delta x enter -3610 mm / for delta y enter -3500 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point

press ‘r’ then ‘e’ / select the corner shown / for delta x enter -3610 mm / for delta y enter -3500 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point
press ‘r’ then ‘e’ / select the corner shown / for delta x enter 2410mm / for delta y enter 1810mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / select the corner previously selected / press y (to restrict to Y axis / for delta Y enter 110 mm / selected enter point/ press ‘Enter
press ‘r’ then ‘e’ / select the corner shown / for delta x enter 2400mm / for delta y enter 1920 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / select the corner previously selected / press y (to restrict to Y axis / for delta Y enter 110 mm / selected enter point/ press ‘Enter

press ‘r’ then ‘e’ / select the corner shown / for delta x enter 2400mm / for delta y enter 600 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / select the corner previously selected / press y (to restrict to Y axis / for delta Y enter 110 mm / selected enter point/ press ‘Enter
press ‘r’ then ‘e’ / select the corner shown / for delta x enter 2400mm / for delta y enter 600 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / select the corner previously selected / for delta x enter 110 mm / for delta y enter -100 / selected enter point/ press ‘Enter’ multiple times

	press ‘r’ then ‘e’ / select the corner shown / for delta x enter 5520mm / for delta y enter -1200 mm / for delta z enter 0 mm / press enter confirming each option/ select enter point / select this rectangle / pre ‘m’ then ‘v’ / enter point/ press ‘Enter’ multiple times
	press ‘r’ then ‘e’ / select the corner shown / for delta x enter 2190mm / for delta y enter -2120mm / for delta z enter 0 mm / press enter confirming each option/ select enter point
	Navigate to the list of windows and doors / press shift E and drag it over w5 / (make sure point snap is on) / press ‘m’ then ‘v’ and select the object at the point shown on the right / select the point labelled 1.
At point 1 place w5

	Select w5 and press ‘m’ then ‘v’ / select the point on d14 as shown in the image to the right / Select(copy)/ press ‘p’ / select point 2 / navigate back to the list of doors and windows using the preferred navigational style

	Select d14 and press ‘m’ then ‘v’ / select the point on d14 as shown in the image to the right / Select(copy)/ press ‘p’ / select point 2 / navigate back to the list of doors and windows using the preferred navigational style

	Press Shift + e select w4 / press ‘m’ then ‘v’ / Select the point shown in the image to the right / select the point 3
at point 3 place w4
	Press Shift+e select all elements of w3 / press ‘m’ then v’ / select the corner as shown / select point 4
place w3 at point 4
	Press shift+e select all elements of w2 / press ‘m’ then ‘v’ / select the corner as shown / select point 5
Place w2 at 5
	Press shift+e select all elements of w2 / press ‘m’ then ‘v’ / select the corner as shown / select point 5
Place w1 at point 6
	Press shift+e, select all elements of w6 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 7
At point 7 place w6
	Press shift+e, select all elements of w6 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 7
At point 8 place w7
	Press shift+e, select all elements of w8 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 16
At point 16 place w8
	Press shift+e, select all elements of w9 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 17
At point 17 place w9	Press shift+e, select all elements of d8 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 9

At point 9 place D8

	Press shift+e, select all elements of d14 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 9
At point 2 place d14

Press shift+e, select all elements of w10 / by dragging the cursor over itpress ‘m’ / then ‘v’ select the point as shown in / the image to the right select point 18
at point 18 place w10

at point 19 place d10	Press shift+e, select all elements of D10 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 19

at point 20 place d9	Press shift+e, select all elements of / D9 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 20
at point 21 place d12	Press shift+e, select all elements of D12 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 21
at point 22 place D13	Press shift+e, select all elements of D12 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 21
at point 23 place D11	Press shift+e, select all elements of D1 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 23
	Press shift+e, select all elements of D1 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 23

	Press shift+e, select all elements of D4 / by dragging the cursor over it press ‘m’ / then ‘v’select the point as shown in the / image to the right select point 11
At point 11 place D4
	Press shift+e, select all elements of D2 / by dragging the cursor over it press ‘m’ / then ‘v’ select the point as shown in the / image to the right select point 12
At point 12 place d2	Press shift+e, select all elements of d2 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 12

at point 13 place d1
	Press shift+e, select all elements of d7 / by dragging the cursor over it / press ‘m’ then ‘v’ / select the point as shown in the image to the right / select point 14
at point 14 place d7

At point 26 place d3

Creating Walls
Setting up
In The toolbar menu Turn Construction mode off by selecting the icon
Make sure the active working plane is the Top one
Make sure snap Grid is selected
Make sure point snap is active

Outer walls
Create outer walls at point A	Pan and zoom to point A / Press ‘p’ then ‘y’ using snap points select the vertexes as shown to the left. ( making sure to create a closed loop / this creates a wire / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data>Draft / Make the make face property true ( this gives the created wire a fill which will be useful later for hatching / select the Wire / option click with the cursor / utilities >move to group>add new name group group / combo view> Tasks> Add group / enter the group name ‘walls’ / select ok

	Pan and zoom so that you can view both points:B and C / Press ‘p’ then ‘y’ using snap points select the vertexes as shown to the left. ( making sure to create a closed loop / this creates a wire / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data>Draft / select the Wire / option click with the cursor / utilities >move to group> / Select walls / (if you have trouble selecting the poly line you can more easily select it in the Combo view
Create outer walls at points B and C
	Pan and zoom so that you can view both points:C and D / Press ‘p’ then ‘y’ using snap points select the vertexes as shown to the left. ( making sure to create a closed loop / this creates a wire / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data>Draft / select the Wire / option click with the cursor / utilities >move to group> / Select walls

Create outer walls at points C and D
	Pan and zoom so that you can view both points:E and D / Press ‘p’ then ‘y’ using snap points select the vertexes as shown to the left. ( making sure to create a closed loop / this creates a wire / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data>Draft / select the Wire / option click with the cursor / utilities >move to group> / Select walls
Create outer walls at points E and F
	Pan and zoom so that you can view points; E, F, G and H / Press ‘p’ then ‘y’ using snap points select the vertexes as shown to the left. ( making sure to create a closed loop / this creates a wire / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data>Draft / select the Wire / option click with the cursor / utilities >move to group> / Select walls
Create outer walls and points; E, F, G and H

	Pan and zoom so that you can view point J / Press ‘r’ then ‘e’ / select any two points arbitrarily / select the rectangle / combo view / this creates a rectangle / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data> / set the height to 800 mm / set the length to 220 mm / set make face to true / select the Wire / option click with the cursor / utilities >move to group> / Select walls / press ‘m’ then ‘v’ and select the vertex shown in the image
Create outer walls at point C3
	Pan and zoom so that you can view point 12 and 13 / Press ‘r’ then ‘e’ / select any the two points shown to the left / select the rectangle / combo view / this creates a rectangle / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data> / set the height to 800 mm / set the length to 220 mm / set make face to true / select the Wire / option click with the cursor / utilities >move to group> / Select walls / press ‘m’ then ‘v’ and select the vertex shown in the image

	Pan and zoom so that you can view points 12, k, L and 6 / Press ‘r’ then ‘e’ / select any the two points shown to the left / select the rectangle / combo view / this creates a rectangle / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data> / set make face to true / select the Wire / option click with the cursor / utilities >move to group> / Walls
Make a wall at points; 12, k, l and 6
	Pan and zoom so that you can view points 12 and 6 / Press ‘p’ then ‘y’ using snap points select the vertexes as shown to the left. ( making sure to create a closed loop / this creates a wire / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data>Draft / select the Wire / option click with the cursor / utilities >move to group> / Select walls
Make a wall between points 12 and 6
	Pan and zoom so that you can view points; P, O, N and M / Press ‘p’ then ‘y’ using snap points select the vertexes as shown to the left. ( making sure to create a closed loop / this creates a wire / Combo-view>Model>Data / select make face and set it to true / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data>Draft / select the Wire / option click with the cursor / utilities >move to group> / Select walls
Make a wall at points M,N, O and P
	Pan and zoom so that you can view point 4 / Press ‘r’ then ‘e’ / select any the two points shown to the left / select the rectangle / combo view / this creates a rectangle / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data> / set make face to true / select the Wire / option click with the cursor / utilities >move to group> / Walls
At point 4 create a wall
	Pan and zoom so that you can view point 4 / Press ‘r’ then ‘e’ / select any the two points shown to the left / select the rectangle / combo view / this creates a rectangle / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data> / set make face to true / select the Wire / option click with the cursor / utilities >move to group> / Walls
At point 3 create A wall
	Pan and zoom so that you can view point 4 / Press ‘r’ then ‘e’ / select any the two points shown to the left / select the rectangle / combo view / this creates a rectangle / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data> / set make face to true / select the Wire / option click with the cursor / utilities >move to group> / Walls

	Pan and zoom so that you can view point 4 / Press ‘r’ then ‘e’ / select any the two points shown to the left / select the rectangle / combo view / this creates a rectangle / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data> / set make face to true / select the Wire / option click with the cursor / utilities >move to group> / Walls

Inner walls
	Pan and zoom so that you can view point 4 / Press ‘r’ then ‘e’ / select any the two points shown to the left / select the rectangle / combo view / this creates a rectangle / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data> / set make face to true / select the Wire / option click with the cursor / utilities >move to group> / Walls
At point 8 create inner walls
	Pan and zoom so that you can view point 4 / Press ‘r’ then ‘e’ / select any the two points shown to the left / select the rectangle / combo view / this creates a rectangle / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data> / set make face to true / select the Wire / option click with the cursor / utilities >

	Pan and zoom so that you can view point 4 / Press ‘r’ then ‘e’ / select any the two points shown to the left / select the rectangle / combo view / this creates a rectangle / select the wire with your cursor ( in the combo menu press ‘t then ‘g’ this navigates to objects selected in the combo view / Combo-view>Model>Data> / set make face to true / select the Wire / option click with the cursor / utilities >

	Select v1and press ‘m’ then ‘v’
Place v1 at C3
	Press ‘c’ then ‘I’,select point C1 / Combo view> Tasks / Set the radius to 150 mm / Combo view>Data>Make Face / set make face value to false
Create a column at C1
	Press ‘c’ then ‘I’,select point C1 / Combo view> Tasks / Set the radius to 150 mm / Combo view>Data>Make Face / set make face value to false
Create A column at C2

Roof Line
	Toolbar>Select construction Mode / press ‘l’ then ‘I’ / combo view> tasks / select the angle check box / set the angle to 45 / select with the mouse far outside the building
Create a 45 degree line at point A
	Toolbar>Select construction Mode / press ‘l’ then ‘I’ / select point B / combo view> tasks / select the angle check box / set the angle to -45 / select with the mouse far outside the building
Create a 45 degree line at point B
	Toolbar>Select construction Mode / press ‘l’ then ‘I’ / select point c / combo view> tasks / select the angle check box / set the angle to -45 / select with the mouse far outside the building
Create a 45 degree line at point C
	Toolbar>Select construction Mode / press ‘l’ then ‘I’ / select point c / combo view> tasks / select the angle check box / set the angle to -45 / select with the mouse far outside the building
Create a 45 degree line at point D
	Toolbar>Select construction Mode / press ‘l’ then ‘I’ / select point c / combo view> tasks / select the angle check box / set the angle to -45 / select with the mouse far outside the building
Create a 45 degree line at point E
	Toolbar>Select construction Mode / press ‘l’ then ‘I’ / select point c / combo view> tasks / select the angle check box / set the angle to -45 / select with the mouse far outside the building
Create a 45 degree line at point F
	Toolbar>Select construction Mode / press ‘l’ then ‘I’ / select point c / combo view> tasks / select the angle check box / set the angle to 45 / select with the mouse far outside the building
Create a 45 degree angle line at G
	Toolbar>Select construction Mode / press ‘l’ then ‘I’ / select point G / combo view> tasks / select the angle check box / set the angle to 45 / select with the mouse far outside the building / select the newly created line an press ‘t’ then ‘r’ and select the top right hand corner of the drawing.
Create a 45 degree angle line at point H
	Toolbar>Select construction Mode / press ‘l’ then ‘I’ / select point C1 / combo view> tasks / select the angle check box / set the angle to 45 / select with the mouse far outside the building / select the newly created line an press ‘t’ then ‘r’ and select the top right hand corner of the drawing.
Create a 45 degree angle line at point C1
	Toolbar>Select construction Mode / press ‘l’ then ‘I’ / select point c / combo view> tasks / select the angle check box / set the angle to 45 / select with the mouse far outside the building

Create a 45 degree angle at point L
	select the line you wish to extend Press ‘t’ then ‘r’ and then select outside of the building
Extend the rooflines beyond the extents of the building
	Assure that the snap intersection snap is on / Assure that construction Mode is toggled on press li and hover your mouse of over the intersecting lines until the snap intersects to restrain the line in the x axsis select out side the buildings floor
Draw a Horizontal Line at the point indicated
	Press ‘l’ then ‘I’ hover the mouse over c until the point snap icon aperas and select it do the same at c / combo view>model> Construction / selec the last line object the folder / select the line and press ’m’ then ‘v’ / [press x / combo view>Tasks / for local delta x enter in 3500 mm22
Draw a line from point c to d and move it
	Press ‘l’ then ‘i’ hover the mouse over the intersection circled in red to the right select the check box for angle and relative / Combo view> tasks / Enter 45 degrees and move the mouse cursor out side the building and press select on the mouse.
	Press ‘l then I’ (using snap points) / select point L / press y and select C1(using snap points) / Combo view>Model>(In the construction folder) / select the line / press ‘o’ then ‘s’ place the mouse cursor to the left side of the object / Combo view>Tasks / enter -3500 for the offset distance / press Enter’
Make a line between points ;C1 and L and offset it
	Press ‘l’ then ‘I’ select the two points